Physics	lab work#2:	How does an ultrasound* work

I. Ultrasound imaging in medicine
The development of the fetus can be …....................................... by routine ultrasounds. An ultrasound is a …..................................... that allows a physician to …............................. internal anatomy through the use of …....................... …......................... ….......................... …........................ A transducer is placed against the skin of the abdomen and gently …..................... …......................... while it emits …...................... sound waves into the body. The sound waves …......................... or echo on structures …......................... the abdomen such as the fetus. The sound wave signals are ….............................. by a computer and …............................ on a monitor. With these images the physician can …........................ the fetus and ….......................... the progress of its development.

*ultrasound: échographie; routine : commun, habituel

II. How ultrasonic waves allow us to « see » through an opaque object ?

1.Equipment: an ultrasonic transmitter, an ultrasonic receiver, sheets of different materials (cardboard, polystyrene, cloth, metal)

2.Experimental setup and measurements:
Connect the transmitter to the power supply, select the pulse mode (“salve”)

1rst column: in front of
- Set the receiver in front of the transmitter; the distance between them should be approximately 20 cms. Connect the receiver to “oscillo5” and adjust the parameters to obverse 1 to 3 pulses.
- Use the cursor to measure the maximum voltage; write down this value in the first cell of the table below.
- Insert each material between the transmitter and the receiver, and measure the maximum voltage value. Write down these values in the first column.
- Draw a schema of one of the experiments.

Fig.1

2nd column: next to
- Set the receiver and the transmitter side by side. Measure the voltage (1srt cell, 2nd column)
- Set each material in front of them approximately at 10 cms and measure the maximum voltage values. Write them down in the second column.
- Draw a schema of one of the experiments.

Fig.2

Material	In front of	Side by side
None
cardboard
metal
polystyrene
cloth
plywood

Understanding:
Indicate if each of these materials transmits or reflects ultrasound waves (Fill in the table with Yes, a lot / Yes, a little / No); Then highlight in red the materials that mostly reflect the signal, and in green those that mostly transmit the signal, in yellow those that do both.
Material	Transmits the wave	Reflects the wave
None
cardboard
metal
polystyrene
cloth
plywood

III. How ultrawaves allow us to measure a distance?

Experimental setup and measurements:
Set the receiver and the transmitter side by side. Set a cardboard in front of them at an “unknown distance”: d
Draw a scheme of the experiment. Indicate the distance d.

Fig.3
- Connect both the transmitter and the receiver to « oscillo5 ».
- Set the parameters of the software in order to see 1 pulse from the transmitter and 1 pulse from the receiver.
  Draw the signals seen on “oscillo5”; identify the signal from the transmitter and the signal from the receiver.

Fig.4
Using the cursor, measure the duration Δt between the beginning of the transmitter’s pulse and the beginning of the receiver pulse. Indicate this duration on the previous picture.

Understanding:
- On the figure 3, indicate the path of the ultrasound wave.
- Which relation links the unknown distance d and end the length of the ultrasound's path L? What is the name of this phenomenon?

Find the formula to calculate the unknown distance d, knowing that the speed of ultrasound in the air is v = 340 m/s.

Does the calculated value of d accord with the experiment?

IV. ultrasound wave path during an ultrasound imaging examination.

As explained in the first paragraph, ultrasound path is affected differently if it encounters a soft organ or a bone.
- When it encounters a gas, as air, the echo is high, and the transmitted wave is low.
- When it encounters a solid, such as bones, the reflexion is total: the echo is very high and the transmission equals zero.
- When it encounters soft organs (muscle), the echo is low; the transmitted wave is high and propagate inside the organ. (all along this propagation, a low echo is sent, and the transmitted wave vanishes progressively).
- When it encounters liquids (such as water), there is no echo; The transmitted wave is high and propagates without sending echoes.

On the following diagrams, the incoming wave is shown in black, the transmitted and the reflected waves are in grey.
1. Highlight the transmitted wave in green and the reflected one in red.
2. Associate the schemes with a gas, a bone, a muscle, water, knowing that longer arrow is, the higher the wave is.
	
	

TO CONCLUDE :
As we know the wave speed, the measurement of the duration between the emission and the reception of a echo allows us to calculate the depth of the organ responsible for the echo.
The amplitude of the echo allows to color the image: the higher the amplitude, the lighter the image. As a consequence, a bone or a gas will appear in white, water in black, and other organs in grey.